## Slide 1
5th International Mine Rescue Conference, Beijing
Thermal Issues in Evacuation and Rescue David Brenkley & Robert Jozefowicz Mines Rescue Service Limited, United Kingdom

## Slide 2: Theme of presentation:
❶ Impacts in rescue (and firefighting)
❷ Impacts in long distance evacuation
❸ Impacts in refuge thermal environment
❹ Increasing refuge cooling effectiveness

## Slide 3: Theme of presentation:
❶ Impacts in rescue (and firefighting)
❷ Impacts in long distance evacuation
❸ Impacts in refuge thermal environment
❹ Increasing refuge cooling effectiveness

## Slide 6
Surface firefighting observations:
Very little data from actual incidents, data comes from exercises
Firefighters can attain high body core temperatures during operations
Rest and recovery periods may not be sufficient to ensure adequate cooling
Maintaining a euhydrated condition is a critical requirement
Active measures for cooling and recovery should be considered
Core body temperature monitoring (heat strain determination) advocated
Guidance on body core temperature action thresholds not agreed yet
Source: UK Fire Research Report 18-2008 (http://www.communities.gov.uk/publications/fire/coretemperature)

## Slide 7
Surface firefighter exposure limits increased by protective clothing:
"Routine exposure" - 100°C, 1kWm-2
"Hazardous exposure" - 160°C, 3-4kWm-2
"Extreme exposure" - 210°C, 10kWm-2
"Critical exposure" >210°C, up to 100kWm-2
Exposure for personnel with light clothing:
• Convection temperature ≤ 60 °C
• Radiation ≤ 2 kWm-2
Issues for underground rescue workers/firefighters: Prewarming travelling inbye, high exercise intensity, weight of BA/equipment, possible thermal radiation, dehydration - leading to fatigue, increased heart rate and hyperthermia

## Slide 8: Theme of presentation:
❶ Impacts in rescue (and firefighting)
❷ Impacts in long distance evacuation
❸ Impacts in refuge thermal environment
❹ Increasing refuge cooling effectiveness

## Slide 9
Simulated evacuation in 100% RH conditions

## Slide 11: Theme of presentation:
❶ Impacts in rescue (and firefighting)
❷ Impacts in long distance evacuation
❸ Impacts in refuge thermal environment
❹ Increasing refuge cooling effectiveness

## Slide 12
Refuge Thermal Environment
Occupancy tests show rapid heat build up and need for cooling (MineARC + MRS RSA tests)
Fundamental advantage of compressed air supplied refuges

## Slide 14
Modelling of carriage thermal conditions during entrapment
(Parsons Brinckerhoff on behalf of London Underground)

## Slide 16: Theme of presentation:
❶ Impacts in rescue (and firefighting)
❷ Impacts in long distance evacuation
❸ Impacts in refuge thermal environment
❹ Increasing refuge cooling effectiveness

## Slide 17
Objective: “How do we make the most efficient use of the compressed air supply to cool the refuge occupants?”

## Slide 18
Refuge thermal environment
Cooling dependent on air flow, wet-bulb temperature, clothing ensemble, metabolic level, number of occupants
Objective: Exploit benefits in increasing local air velocity

## Slide 19
- Generic case of high capacity fixed underground refuge using section of roadway
- Longitudinally ventilated by compressed air

## Slide 20
- Low relative velocity of fresh air moving through refuge.
- Air speed at skin surface may be <0.5 m/s.

## Slide 21
- Use of four annular air amplifiers shown
- Significant local recirculatory air flow
- Turbulence ensures maximum cooling effect

## Slide 23
Investigation programme …
❶ Select air delivery flow rates
❷ Measure air velocity sectional profiles
❸ Measure refuge sound levels
❹ Undertake microclimate benefit analysis
❺ Assessment of mine implementation issues

## Slide 24
Consumer version of ‘air amplifier’

## Slide 26
Industrial version of ‘air amplifier’

## Slide 34
Cooling characteristic – 12 occupants

## Slide 36
Spectogram Speech only

## Slide 37
Spectogram Speech + Compressed Air Noise @ 5 bar

## Slide 38
CONCLUSIONS & RECOMMENDATIONS:
❶ Thermal impacts during rescue, firefighting, evacuation and refuge each need to be taken account of
❷ International dimension to problem in deep mines
❸ Refuges/mustering stations to be considered as an integral component of emergency evacuation planning
❹ Use of ‘air amplifiers’ for compressed air supplied refuges appears a promising technology
❺ Recommend reading associated MRSL paper – which provides further discussion

## Slide 39
Thank You