## Slide 1
October 5th – 10th, 2013
Denis G. Beaudoin Corporate Director – Health & Safety
Cementation Canada Inc.
International Mine Rescue Conference Niagara Falls, Ontario, Canada
Mining Contractor’s Perspective on Mine Rescue / Emergency Preparedness

## Slide 2: Agenda
Introduction
History
Regulations
Challenges
Situation
Actions
Solutions
Emergency Guideline

Questions

## Slide 3: Introductions
Denis Beaudoin – Corporate Director, H&S Cementation Canada Inc. includes Cementation U.S.A. & Cementation Sudamerica
Sec. Treasurer – Ontario Mine Contractors Safety Association (OMCSA), Mines Accident Prevention Association Manitoba (MAPAM), – Association d’Entreprenuer Miner Québec (AEMQ)
Canadian Society of Safety Engineers (CSSE)

## Slide 4: Mining Contractors Perspective Mine Rescue History – An Overview
Small projects, client provide coverage
Large projects, client provides coverage
Large Turn Key Operations
Small Turn Key Operations
Mine Rescue Coverage
Regulatory Requirements for Mine Rescue
Notes: Presenter
2013-07-11 20:18:38
--------------------------------------------
History has proven that the various mine rescue situations that the mining contractors tend to find themselves in, has not changed much in Canada over the most recent years. The situations we tend to find ourselves in, change slightly based on the scope of work.
In small projects, clients tend to provide coverage, in large projects, clients still tend to provide coverage; but due to the availability of contractor workers, contractors provide a few key mine rescue personnel to be part of the response team. Although, the Client still accommodates the mine rescue personnel from the contractors with a refresher training. On large turnkey operations, usually the contractor arranges for enough trained mine rescue personnel to provide coverage, and at times may request or develop mutual aid agreements with any nearby mining properties.
On small turnkey operations, there are not enough contractor workers to provide mine rescue coverage, which leaves the mining contractor with no other alternative than to arrange for mutual aid agreements from mining properties close by, and to deliver an emergency response plan to workers on how to cope in an emergency situation. Also in remotely located smaller projects , where there are not enough workers to make a mine rescue team, example, small bulk sample projects, one heading ramp adits, raise climber installations, shaft sinking operations etc.
Yet the way the regulations are written, it makes things very difficult for the mining contractor to comply with the regulations.

## Slide 5: Mining Contractors Perspective Mine Rescue History
The most recent incident involving a serious fire at a shaft sinking project was “ Victor Deep”
The investigation of the event caused certain recommendations to be implemented to prevent certain actions from occurring again
Notes: Presenter
2013-07-11 20:18:42
--------------------------------------------
Such as:
Fire Resistant Hydraulic Oils. Fire Suppression Systems
Remove and replace combustibles with non-combustible material Replace rope type bell wire with Aircraft cable, that will not burn
Replace High Temperature Lights in the shaft with lower temperature bulbs, and also ensure that all light fixtures have a cover over the bulb. Maintain workplace free of combustibles, as well as good housekeeping, remove excessive grease, or oil buildups.

## Slide 6: Mining Contractors Perspective Mine Rescue Regulations
Most Provincial and Territorial Regulations require that the mine owner ensures a sufficient amount of workers are trained in Mine Rescue Operations, and available to provide rescue operations in a timely fashion
Notes: Presenter
2013-07-11 20:18:42
--------------------------------------------
The responsibility for mine rescue coverage at a mine belongs to the mine owner; however, this responsibility is passed on to the mining contractor when the mine owner does not have workers on the mining project that is being operated mostly by mining contractors.

## Slide 7: Mining Contractors Perspective Mine Rescue Challenges — 1
Size of Project
Type of Project
Manpower
Remote Locations
Duration of Project
Age of Workforce
Manpower Flow Through
Notes: Presenter
2013-07-11 20:18:42
--------------------------------------------
As stated earlier, these are some of the challenges, such as: Varied project sizes — small, medium, large.
Small projects, - not enough workers to make up one team. Medium projects, may have two teams, but not readily available.
Large Projects- not a problem with number of workers, training, or availability, but the type of project may decide if even with a large project, whether it is possible.

## Slide 8: Mining Contractors Perspective Mine Rescue Challenges — 2
The types of projects in themselves become a challenge:
Shaft Sinking
Single Heading Adits
Single Alimak Heading
Construction, De- watering projects

## Slide 9: Mining Contractors Perspective Mine Rescue Challenges — 3
The type and size of the project will determine manpower
Is there a sufficient number of workers to
make up at least
two teams…can the project progress, training to be conducted?
and still allow for
What about remote locations, small projects, minimum manpower, response times
Short duration projects
Notes: Presenter
2013-07-11 20:18:42
--------------------------------------------
If the mining contractor provides the mine rescue coverage at a project, where it may be possible to have two teams, available at all times, even during turnaround time, the client has to accept the production schedule to allow for the teams to train.
Even with 2 teams, the 1st team responds to an emergency situation, and the 2nd team remains on standby, until a 3rd emergency response team arrives to be on standby. Only then, can the 2nd team go after the 1st team, should the 1st team encounter problems.

## Slide 10: Mining Contractors Perspective Mine Rescue Challenges — 4
Age of the workforce, most cannot pass the medical exam.
Contract Miners, tend to move around, based on the wages paid at other sites.
10

## Slide 11: Mining Contractors Perspective Mine Rescue Challenges — 5
Shaft Sinking Buckets
Clients
Mine
Rescue
personnel
Access to an Alimak.
11
Notes: Presenter
2013-07-11 20:18:43
--------------------------------------------
Shaft sinking, most shaft buckets cannot accommodate a whole emergency rescue team. Most mine rescue personnel (if) provided by the client are not familiar with shaft sinking
Most mine rescue personnel are unaccustomed to entering or exiting a bucket, or have experience/ awareness of a Galloway. Mine rescue personnel not familiar with raise climbers , attempting to rescue a raise climber ( Alimak ) personnel.
These are just a few of the challenges…

## Slide 12
Shaft
Sinking – 50
Workers Total
Alimak Operation – 10 workers
Single heading adits
Construction De- watering projects 10 workers
Open Pit Operation, total workforce including supervision 18 workers
12
Mining Contractors Perspective Mine Rescue Situations — 1
Notes: Presenter
2013-07-11 20:18:43
--------------------------------------------
A single shaft operation includes about 12 workers per shift: hoist operator
shaft miners electricians, mechanics deckman & welder.
Project Manager, Shaft Superintendent, Shaft Technician /Surveyor, on dayshift
¼ is on turnaround (R&R)
Support staff, includes buyer/ clerk, and safety & training coordinator. includes perhaps, 6 raise miners, 2 on R&R, 3 mechanics, 1 on R&R.

## Slide 13
Typically a fire emergency in a shaft, becomes a recovery, not a rescue, if systems are not in place prior to the event.
We need a plan!!!!
Mining Contractors Perspective Mine Rescue Situations — 2

## Slide 14: Mining Contractors Perspective Mine Rescue Actions—1
Some
members from the OMCSA participated in a
committee, consisting of representatives from two large Mining Operators, as well as the Ministry of Labour and MASHA Mine Rescue Officers to review all of the issues related to Mine Rescue coverage for Mining Contractors, at shaft sinking projects.
The committee reviewed, and discussed the challenges faced by contractors related to providing Mine Rescue coverage.

## Slide 15: Mining Contractors Perspective Mine Rescue Actions—2
Based on the review an Emergency Preparedness Shaft Sinking Guideline was developed.
The guideline only dealt with a shaft sinking operation.
There still is a requirement to deal with all the other situations presented here today
THAT IS OUR CHALLENGE, WHAT ARE WE GOING TO DO ABOUT IT!!!!!

## Slide 16: Mining Contractors Perspective Mine Rescue Solutions—1
Train a percentage of workers at the shaft sinking project in the use of a SCBA, as well as training all workers in the emergency response plan.
Ensure that First Aid and CPR training is available.
Provide a rescue bucket with a 100 lb. bottle of air, and a 50ft. umbilical line.
Supply the shaft project with a sufficient amount of oxygen generating self-rescuers, strategically placed on the Galloway and equipping basket.

## Slide 17: Mining Contractors Perspective Mine Rescue Solutions—2
Reduce combustible materials in shaft sinking.
Use Fire Retardant Hydraulic Oils.
Have Automatic Fire Suppression Systems on power packs.
Reduce the amount of heat from light fixtures.
Arrange for mutual aid agreements.
Develop Emergency Preparedness Plans for all projects, big or small.

## Slide 18
I would like to thank the IMRC committee , for allowing me the opportunity to speak to you today.
QUESTIONS?