## Slide 1
Oct 8, 2013 IMRB 2013 Conference
Strategy.
Discipline.
Execution.

## Slide 2: Portable Refuge Chambers vs Permanent Refuge Stations
To create a safe environment that will sustain our workforce that are trapped underground during an emergency.
Objective

## Slide 3: Portable Refuge Chambers vs Permanent Refuge Stations
History of Refuge Stations and Refuge Chambers
Hard Rock
Redundant cutouts with a barrier wall(s) creating an area that could be over-pressurized
Areas of sufficient size to utilize ‘dead air space’ as an air supply.
Perhaps adding compressed oxygen
from cylinders and CO2 removal
Located in close proximity to work headings
Higher cost, slower rate of construction
Can house more personnel for set period of time

## Slide 4: Portable Refuge Chambers vs Permanent Refuge Stations
History of Refuge Stations and Refuge Chambers
Hard Rock
As work areas shift quickly, refuge areas need to as well
Trend moving towards portable refuge chambers / shelters
Requires smaller sized opening for placement
Mobility, cost effectiveness, climate controlled
Offers life support even if main mine support services are lost
Higher degree of quality control in
construction

## Slide 5: Portable Refuge Chambers vs Permanent Refuge Stations
Operational Review
In fresh air ventilation flow (if possible)
Determine sizing:
  # of workers in the area (employees and visitors)
  ‘Dead air space’ vs stored O2 supply
Determine spacing of refuge areas
Infrastructure in the area (electrical subs, shops, fuel bays, explosives storage etc)
Assured supply of compressed air
Located on main travel route for the area being serviced

## Slide 6: Portable Refuge Chambers vs Permanent Refuge Stations
Operational Review
Determine length of time the refuge area will be in service (short / long term)
Vehicle traffic (damage, access)
Local regulatory requirements
Ambient rock temperatures
Length of time to construct permanent refuge station
Determine size of opening for permanent vs portable
Access to communication systems, power supply
Ground conditions – competent ground in the area

## Slide 7: Portable Refuge Chambers vs Permanent Refuge Stations
Vestibule
Access lighting
Interior lighting
Exterior door opens outward
Interior door opens inward
Gas monitoring in vestibule (CO, O2), chamber (CO, CO2 O2)
Positive pressure capability in vestibule and in chamber (compressed air cylinders)
Pressure relief in vestibule and chamber
Portable Refuge Chambers – features to consider

## Slide 8: Portable Refuge Chambers vs Permanent Refuge Stations
Oxygen supply
CO2 removal
Thermal protection
Double walls
Independent battery system
Climate control (heater/ air conditioning)
Set duration of Life Support System
  O2 supply
  electrical supply (in emergency mode)
Portable Refuge Chambers – features to consider

## Slide 9: Portable Refuge Chambers vs Permanent Refuge Stations
Set # of occupants
Potable water
Toilet facilities
Transport capabilities
Entertainment package
After market support engineering
service / training
Portable Refuge Chambers – features to consider

## Slide 10: Portable Refuge Chambers vs Permanent Refuge Stations
Determine best suited solution for site specific needs
Settle for only top quality products / workmanship (life safety units)
Maintenance program
Acceptance and psychological adjustment by workforce
  Smaller size
  mechanical life support system
Conclusion