## Slide 1
Development of
Emergency Prevention & Response Plan
Alexander Sin, PhD
Member of the International Academy of Ecology
and Life Protection Sciences
Head of Mines Rescue Services Department of Emercom of Russia
Niagara Falls, 2013
International Mines Rescue Body Conference 2013

## Slide 2
Main disadvantages of currently applied Emergency Response plans
Substantive provision of the Emergency Response Plan and ventilation scheme contains a lot of preplanned response procedures, made for the workings where emergencies practically never happen, moreover it contains a lot of single-type actions repeated nearly in every preplanned response procedure;
To identify the volume of mine workings being gassed often becomes impossible in case of explosion in the mine. At the initial stage this matter decrease operational efficiency of mine rescue teams arrived for examination of the emergency place in order to provide first aid to the injured miners
It is very difficult to choose the right preplanned emergency procedure of the Emergency Response Plan in short period of time if there are no accurate information about the location of fire or explosion
Emergency Response Plan is aimed to carry out the actions that can help to decrease potential consequences of occurred emergency situation, but has no actions that could prevent an emergency itself.
Slide: 2

## Slide 3
A lot of emergency situations are developing during several working shifts, days and even weeks, that is why operations superintendent needs document, that will allow to control dangerous areas in the mine, equipment and machineries in real-time mode.
For this purpose we suggest to apply
“Emergency Prevention and Response Plan”.
The fundamental part of this document is devoted to the approach of identification potential hazards.

## Slide 4
Structure of
Emergency Prevention and Response Plan
Text part
Substantive provision
Preplanned Emergency Procedure
Plans of prognosis of rock conditions in longwall and drifting faces
Liquidating part
Preventive part
Informative part: reflects potential risks that may occur during operations and that can turn into emergency situation
Operational part: contains inspection data of mine rescue equipment
Drawings
Layouts of mine roadways
Surface plan
Plans of mining works
by the strata and levels
Ventilation Scheme
Слайд: 4
Contains actions aimed to eliminate occurred accident and information about mine rescue team’s work
Attachments: 1. Minutes of engineering meeting headed by the Chief engineer of the mine.
2. Inspection acts.

## Slide 5
Preventive Part of
preplanned emergency procedure
Slide : 5

## Slide 6
Preventive part. Plans of prognosis of rock conditions
in longwall face
Slide : 6

## Slide 7: Filling of the Preventive part of the preplanned emergency procedure is done by a mine foreman. Before the mine foreman begins his work he learns information recorded in the Preventive part of the preplanned emergency procedure by the mine foreman of the previous shift and gets “The Work order for the shift” with a control form printed on its back-page . The control form is filled in during the shift by the mine foreman. At the end of the working shift the mine foreman transfer all data from the control blank to the Preventive part of the emergency procedure and signs it up. The control form should be filed into a special folder and kept for at least 3 months.
Slide : 7

## Slide 8
Control Form
Slide : 8

## Slide 9
Drawings.
Ventilation Scheme
Slide : 9
From the end of every planned emergency procedure along the direction of the return ventilation air up to the exit to the surface colored lines are drawn on the Ventilation scheme
Alarm sensors

## Slide 10: Alarm sensors are installed at the following places in the mine:
- near the exits to the surface;
- at the places of air split;
- at the beginning and at the end of the heading where there is a risk of hazards;
- at different points of extended parallel routes;
- at the points where reverse ventilation ends
Slide: 10

## Slide 11
Slide : 11
Common arrangements of Emergency Prevention and Response Plan
№ | Life-rescue actions, applied at emergency situation | Person responsible for actions and performer
1 | To call Mine rescue team according with the list №1 | Mining dispatcher
2 | Provide arrival of mine rescue teams, paramedics, vehicle equipped with firefighting equipment | Mine rescue captain, dispatcher
3 | Fan at South-West shaft work in regular mode | Chief mechanic
4 | Power cutoff at all mine roadways | Chief power engineer
5 | Members of auxiliary mine rescue teams ask dispatcher for detailed information about the place of emergency occurrence: In case of fire: with breathing apparatus and fire extinguishers go to roadway from the side of intake air to the fire source for firefighting. Water for firefighting is taken from fire pipe-line located at the ventilation shaft 1324. | Officer in charge of mine rescue operations regulation
 | In case of explosion: with breathing apparatus go to emergency roadway to rescue people. People are evacuated to the nearest intake air and then to the surface | 
6 | To notify everyone in the mine about emergency and about evacuation to the surface by escape exits. | Dispatcher
7 | Provide lifting of the miners from underground, descending Mine rescue team to the South-West shaft. | Chief Mechanic, other underground workers
8 | Organize safety command centers at the following places: South-West shaft; Inclined roadway 2; Conveyor inclined roadway 19. To forbidden entrance to the mine for people, who don’t have passes | Officer in charge of mine rescue operations regulation
9 | Evacuate people: by escape exits from their workplaces; to the nearest intake air and then to the surface | Officer in charge of mine rescue operations regulation

## Slide 12: Advantages of Emergency Prevention and Response Plan
Helps to make workers of the mine deal with safety issues on a regular basis
Allows to choose the right preplanned emergency procedure faster
Accumulates information that helps to make detailed evaluation and identify problems that can cause an occurrence of emergency situation
Helps to identify pre-emergency situations in time and prevent occurrence of its potential consequences
Slide : 12

## Slide 13
Thank you for Attention!